## Slide 1
Bharat Electronics
www.bel-india.in

## Slide 2
VVPAT
Features of
M3 VOTER VERIFIABLE PAPER AUDIT TRAIL
(VVPAT - M3)

## Slide 3
Features of M3 VVPAT
VVPAT

## Slide 4
VVPAT - Introduction
The elections in India are currently held using EVMs and counting is based on the results obtained in the EVM.
The purpose of the Voter Verifiable Paper Audit Trail (VVPAT) System is to print the selection of the voter on a slip for the voter to visually verify the vote cast.
Voter Verifiable Paper Audit Trail (VVPAT) system is a printer based accessory used in the set up of Electronic Voting Machine (EVM).
The VVPAT system prints the voter’s franchise on a thermal paper ballot slip for voter verification when EVMs are used in elections as well as an audit trail.
Introduction of the VVPAT

## Slide 5
VVPAT- features
Special Features of the VVPAT
When the VVPAT system is used in combination with the EVM, it provides verification to the voter by way of printing the cast vote on a thermal paper ballot slip.
When the voter presses the button on the Ballot Unit (BU) to vote for the candidate of his / her choice, the VVPAT system prints a ballot slip of size 99 mm length.
The printed ballot slip is visible to the voter for a period of 7 seconds through a screen window available on VVPAT.
The ballot slip is then cut by the VVPAT unit and made to fall into the Ballot Slip compartment.

## Slide 6
VVPAT- features
VVPAT system consists of four independent compartments,
namely :
(i) Paper roll compartment (ii) Ballot slips compartment
(iii) Battery compartment (iv) Connector compartment
Special Features of the VVPAT

## Slide 7
VVPAT- features
Prints the ballot slip of size 56 x 99 mm
Operates on a battery pack (22.5 V / 4 Ah)
Accommodates paper roll of length 150 meters or less
Special Features of the VVPAT

## Slide 8
VVPAT – Ballot Slip
Ballot slip contains Information's:
Serial number of the contesting candidate
Name of the candidate selected
Corresponding election symbol
Serial number of the VVPAT unit
Poll session number

## Slide 9
VVPAT – Carrying Cases
VVPAT is packed separately in special carrying cases
Carrying Case - VVPAT
To Open the Carrying case, Lift front and side latch

## Slide 10
Front View
VVPAT – Front View
Ballot Slip Compartment
The Interconnecting cable is permanently attached to the VVPAT Unit
Transparent Window
Power ON LED

## Slide 11
Connector and Battery Compartment
VVPAT– Rear View
Connector
Compartment
Battery
Compartment
VVPAT Position Switch
Battery Plug
BU interface

## Slide 12
VVPAT- Rear View
Battery Insertion
BU cable connected
Position Switch in 1(Left side

## Slide 13
VVPAT–Rear View
Keep know horizontal while
transporting VVPAT
Keep know vertical while using VVPAT
Lock-Unlock Knob
Stickers for Indication

## Slide 14
VVPAT – Opening of Paper Compartment
Paper Compartment
after opening
Lift side Latch to
open Compartment

## Slide 15
Loading of Paper Rolls
VVPAT
Insert spindle into
Paper Roll
Press down Paper Roll into space provided
Insert Paper into
Paper Guide

## Slide 16: VVPAT Connection
Open connector compartment of VVPAT
Connect cable from Ballot Unit to BU Interface connector matching the coloured latches (red/black connector)
Connect VVPAT cable to BU interface connector of Control Unit matching the coloured latches (red/black connector)

## Slide 17
VVPAT setup with CU and BU
VVPAT

## Slide 18
THANK YOU
VVPAT
www.bel-india.in